## Slide 1
ME 224
STRENGTH OF MATERIALS
Assoc. Prof. Dr. Nurettin Furkan DOĞAN
Department of Mechanical Engineering
E-mail: nfdogan@gantep.edu.tr
Office: Mechanical Engineering Department Building
4th Floor, No: 303

## Slide 2: Course Description
STRENGTH OF MATERIALS ME 224
Credit Structure: (3-1)4
Course Objectives:
The main objective of the course is to develop in the second-year mechanical engineering students a clear understanding of relationship between the loads applied to elastic bodies, and the resultant stresses, strains and deformations.
Prerequisities:
ME 201 Statics
Textbook(s):
F.P. Beer and E.R. Johnston, “Mechanics of Materials”,
McGraw-Hill Int Book Company
Reference:
R.C. Hibbeler, "Mechanics of materials", Prentice Hall Inc, 1997
Instructors: Prof. Dr. Ömer Yavuz BOZKURT, Assoc. Prof. Dr. Nurettin Furkan DOĞAN
Exams: 1. Midterm 30% ;2. Midterm 30% ; Final: 40%
Attendance: The attendance of 70% is mandatory.
E-mails : oybozkurt@gantep.edu.tr
nfdogan@gantep.edu.tr

## Slide 3
INTRODUCTION | 25.02.2025 | EXAMS First and Second Examination dates will be announced by the department. Textbook Mechanics of Materials By Ferdinand P. Beer and E. R. Johnston Auxiliary Books Mechanics of Materials By R.C. Hibbeler Many books related with the Strength in the Library
Ch 1. Normal, Shear stress | 28.02.2025 | 
Ch 1. Oblique Plane,Factor of Safety | 04.03.2025 | 
Ch 1. Pr.Hr. | 07.03.2025 | 
STRESS AND STRAIN Ch 2. Stress-Strain- Deformation | 11.03.2025 | 
Ch 2. Pr.Hr. | 14.03.2025 | 
Ch 2. Statically Indeterminate Pr. | 18.03.2025 | 
Ch 2. Poissons’ Raito and so on | 21.03.2025 | 
Ch 2. Pr.Hr. | 25.03.2025 | 
TORSION Ch 3. Torsion | 28.03.2025 | 
Ch 3. Pr.Hr. | 04.04.2025 | 
Ch 3. Power Transmission | 08.04.2025 | 
PURE BENDING Ch 4. Pure Bending | 11.04.2025 | 
Ch 4. Pr.Hr. | 15.04.2025 | 
Ch 4. Eccentic Axial Loading | 18.04.2025 | 
Ch 4. Pr.Hr. | 22.04.2025 | 
FIRST EXAM | --.--.---- | 
2024-2025 SPRING SEMESTER ME 224 GENERAL CONTENT

## Slide 4
SHEARING STRESS Ch 6. in Beams | 29.04.2025 | EXAMS First and Second Examination dates will be announced by the department. Textbook Mechanics of Materials By Ferdinand P. Beer and E. R. Johnston Auxiliary Books Mechanics of Materials By R.C. Hibbeler Many books related with the Strength in the Library
Ch 6. Pr.Hr. | 02.05.2025 | 
Ch 6. in Thin walled members | 06.05.2025 | 
Ch 6. Pr.Hr. | 09.05.2025 | 
PRINCIPAL STRESSES UNDER A GIVEN LOADING Ch 8. Combined Loadings | 13.05.2025 | 
Ch 8. Pr.Hr. | 16.05.2025 | 
TRANSFORMATION OF STRESS Ch 7. Transformation of Plane Stress and Mohr’s Circle | 20.05.2025 | 
Ch 7. Pressure Vessels and Yield Criteria’s | 23.05.2025 | 
Ch 7. Pr.Hr. | 27.05.2025 | 
DEFLECTION OF BEAMS Ch 9. Integration (Deflection of Beams) | 30.05.2025 | 
Ch 9. Singularity Function(Deflection of Beams) | 03.06.2025 | 
Ch 9. Singularity Function(Deflection of Beams) | --.--.---- | 
Ch 9. Pr. Hr. | --.--.---- | 
SECOND EXAM | --.--.---- | 
2023-2024 SPRING SEMESTER ME 224 GENERAL CONTENT

## Slide 5
Chapter 1- Introduction Concept of Stress

## Slide 6: Mechanics In Science
Mechanics is one the essential branch in physics. It can be examining in solid mechanics and fluid mechanics.
Rigid Bodies
Deformable Bodies
Statics
Dynamics
Elasticity
Thermo-elasticity
Fracture
Plasticity
. . . . .
Under Some simplification assumptions
(Geometry; Boundary Conditions; Material model simplifications)
Mechanics of Materials
Mechanics
Fluid Mechanics
Solid Mechanics
Advanced Mechanics of Materials

## Slide 7: Main Objective of Mechanics of Materials
The main objective of the study of mechanics of materials is to provide the future engineer with the means of analyzing and designing tips various machines, machine elements and structures.
Both the analysis and design of a given structure involve the determination of stresses and deformations.

## Slide 8: Method of Analysis
APPLIED LOAD
DEFORMATION
STIFFNESS
STRESS
STRAIN
COMPATIBILITY
CONSTITUTIVE
EQUILIBRIUM
STRUCTURE

## Slide 9: Review of Statics
Statics has two main goals:
Introduction to basic concepts of force, couples and moments in two and three dimensions structures.
Developments of analytical skills relevant to the areas of mentioned in above.

## Slide 10: Example in Statics
Determine the internal force in each structural member and the reaction forces at the supports
The structure consists of a boom (50mm x 30 mm) and rod (d=20mm) joined by pins at the junctions and supports

## Slide 11: Structure Free-Body Diagram
Structure is detached from supports and the external loads and reaction forces are indicated
Conditions for static equilibrium:
Ay and Cy can not be determined from these equations

## Slide 12: Component Free-Body Diagram
In addition to the complete structure, each component and each point must satisfy the conditions for static equilibrium
Results:
Reaction forces are directed along boom and rod
Consider a free-body diagram for the boom:
substitute into the structure equilibrium equation

## Slide 13: Method of Joints
Alternative Solution Of Using Two Force Members Concept
The boom and rod are 2-force members, i.e., the members are subjected to only two forces which are applied at member ends
Joints (points) must satisfy the conditions for static equilibrium which may be expressed in the form of a force triangle:
For equilibrium, the forces must be parallel to to an axis between the force application points, equal in magnitude, and in opposite directions

## Slide 14: Axial Loading: Normal Stress
The force intensity (force per unit area) on that section is defined as the normal stress, (sigma).
Consider an axially loaded member. The resultant of the internal forces for an axially loaded member is normal to a section cut perpendicular to the member axis.
Average Normal stress in a member under axial loading
A positive sign indicates a tensile stress (member in tension), and a negative sign indicates a compressive stress (member in compression).

## Slide 15: Normal Stress in Axially Loaded Members
The normal stress at a particular point may not be equal to the average stress but the resultant of the stress distribution must satisfy
To define the stress at a given point Q of the cross section, consider a small area
The detailed distribution of stress is statically indeterminate, i.e., can not be found from statics alone.
Notes: In a slender rod subjected to equal and opposite concentrated loads P and P’ (Fig. 1.10a), this variation is small in a section away from the points of application of the concentrated loads (Fig. 1.10c), but it is quite noticeable in the neighborhood of these points (Fig. 1.10b and d).

## Slide 16: Centric & Eccentric Loading
If a two-force member is eccentrically loaded, then the resultant of the stress distribution in a section must yield an axial force and a moment.
The stress distributions in eccentrically loaded members cannot be uniform or symmetric.
A uniform distribution of stress in a section infers that the line of action for the resultant of the internal forces passes through the centroid of the section.
A uniform distribution of stress is only possible if the concentrated loads on the end sections of two-force members are applied at the section centroids. This is referred to as centric loading.

## Slide 17: Stress Analysis
Conclusion: the strength of member BC is adequate
From the material properties for steel, the allowable stress is
Can this structure safely support the 30 kN load?
At any section through member BC (except connection region), the internal reaction force is 50 kN with a force intensity or stress of
dBC = 20 mm
From a statics analysis
FAB = 40 kN (compression)
FBC = 50 kN (tension)
1.b. Stress analysis for the BC member (except connection region)

## Slide 18: Design
For reasons based on cost, weight, availability, etc., the choice is made to construct the rod from aluminum (sall= 100 MPa). What is an appropriate choice for the rod diameter?
An aluminum rod 26 mm or more in diameter is adequate
1.c. Design for the BC member (Changing material from steel to aluminum)

## Slide 19: Shearing Stress
Force P is applied transversely to the member .
The corresponding average shear stress is,
The resultant of the internal shear force distribution is defined as the shear of the section and is equal to the load P.
Corresponding internal forces act in the plane of section A and are called shearing forces.

## Slide 20: Shearing Stress Examples

## Slide 21: Shearing Stress Examples

## Slide 22: Bearing Stress in Connections
Bolts, rivets, and pins create stresses on the points of contact or bearing surfaces of the members they connect.
Corresponding average force intensity is called the bearing stress,
The resultant of the force distribution on the surface is equal and opposite to the force exerted on the pin.

## Slide 23: More on Bearing Stress

## Slide 24: Linkage in Tension and Compression
Force is affecting the hatched area under tension.
For this case, circular part is also checked.
Force is affecting the hatched area under compression

## Slide 25: Stress Analysis & Design Example
Would like to determine the stresses in the members and connections of the structure shown.
Must consider maximum normal stresses in AB and BC, and the shearing stress and bearing stress at each pinned connection
From a statics analysis:
FAB = 40 kN (compression)
FBC = 50 kN (tension)
1.d. A complete Stress analysis for the AC and BC member (including connection region)

## Slide 26: Rod & Boom Normal Stresses
The rod is in tension with an axial force of 50 kN.
The boom is in compression with an axial force of 40 kN and average normal stress of –26.7 MPa.
The minimum area sections at the boom ends are unstressed since the boom is in compression.
At the flattened rod ends, the smallest cross-sectional area occurs at the pin centerline,
At the rod center, the average normal stress in the circular cross-section (A = 314x10-6m2) is sBC = +159 MPa.

## Slide 27: Pin Shearing Stresses
The cross-sectional area for pins at A, B, and C,
The force on the pin at C is equal to the force exerted by the rod BC,
The pin at A is in double shear with a total force equal to the force exerted by the boom AB,

## Slide 28: Pin Shearing Stresses
Divide the pin at B into sections to determine the section with the largest shear force,
Evaluate the corresponding average shearing stress,

## Slide 29: Pin Bearing Stresses
To determine the bearing stress at A in the boom AB, we have t = 30 mm and d = 25 mm,
To determine the bearing stress at A in the bracket, we have t = 2(25 mm) = 50 mm and d = 25 mm,

## Slide 30: Stress in Two Force Members
We will show that either axial or transverse forces may produce both normal and shear stresses with respect to a plane other than one cut perpendicular to the member axis.
Axial forces on a two-force member result in only normal stresses on a plane cut perpendicular to the member axis.
Transverse forces on bolts and pins result in only shear stresses on the plane perpendicular to bolt or pin axis.

## Slide 31: Stress on an Inclined Plane
Pass a section through the member forming an angle q with the normal plane.
The average normal and shear stresses on the inclined plane are
Resolve P into components normal and tangential to the inclined section,
From equilibrium conditions, the distributed forces (stresses) on the plane must be equivalent to the force P.

## Slide 32: Maximum Stresses
The maximum normal stress occurs when the reference plane is perpendicular to the member axis,
The maximum shear stress occurs for a plane at + 45o with respect to the axis,
Normal and shearing stresses on an inclined plane

## Slide 33: Stress Under General Loadings
A member subjected to a general combination of loads is cut into two segments by a plane passing through Q
For equilibrium, an equal and opposite internal force and stress distribution must be exerted on the other segment of the member.
The distribution of internal stress components may be defined as,

## Slide 34: State of Stress
Stress components are defined for the planes cut parallel to the x, y and z axes. For equilibrium, equal and opposite stresses are exerted on the hidden planes.
The combination of forces generated by the stresses must satisfy the conditions for equilibrium:
It follows that only 6 components of stress are required to define the complete state of stress
Consider the moments about the z axis:

## Slide 35
Normal stress is indicated with this symbol
Shearing stress is indicated with this symbol
These indices show the axis parallel to the normal of the surface on which the stress acts.
These indices show the axis to which the stress is parallel.

## Slide 36: Allowable Load and Allowable Stress: Factor of Safety
Structural members or machines must be designed such that the working stresses are less than the yield strength of the material.
The maximum load that a structural member or a machine component will be allowed to carry under normal conditions is considerably smaller than the ultimate load. This smaller load is the allowable load (sometimes called the working or design load).
The ratio of the ultimate load to the allowable load is used to define the factor of safety:

## Slide 37
Free-body diagram of bracket.
Sample Problem
Two loads are applied to the bracket BCD as shown. (a) Knowing that the control rod AB is to be made of a steel having an ultimate normal stress of 600 MPa, determine the diameter of the rod for which the factor of safety with respect to failure will be 3.3. (b) The pin at C is to be made of a steel having an ultimate shearing stress of 350 MPa. Determine the diameter of the pin C for which the factor of safety with respect to shear will also be 3.3. (c) Determine the required thickness of the bracket supports at C, knowing that the allowable bearing stress of the steel used is 300 MPa.
Using free-body diagram of bracket:

## Slide 39
The 1.4-kip load P is supported by two wooden members of uniform cross section that are joined by the simple glued scarf splice shown. Determine the normal and shearing stresses in the glued splice.
EXERCISE 1.
EXERCISE 2.
Two wooden members of uniform cross section are joined by the simple scarf splice shown. Knowing that the maximum allowable tensile stress in the glued splice is 75 psi, determine (a) the largest load P that can be safely supported, (b) the corresponding shearing stress in the splice.

## Slide 40
Link AB is to be made of a steel for which the ultimate normal stress is 65 ksi. Determine the cross-sectional area of AB for which the factor of safety will be 3.20. Assume that the link will be adequately reinforced around the pins at A and B.
EXERCISE 3.
Link BC is 6 mm thick, has a width w = 25 mm, and is made of a steel with a 480-MPa ultimate strength in tension. What is the factor of safety used if the structure shown was designed to support a 16-kN load P?
EXERCISE 4.