## Slide 1: FOOD QUALITY CONTROL
FE 376
Prof. Dr. Emine ERÇELEBİ
Notes: 1

## Slide 2
Size and shape are important physical attributes of foods that are used in:
-screening
-grading
-quality control of foods
-fluid flow
-heat and mass transfer calculations for food operations
        SIZE, SHAPE, VOLUME and Related Attributes

## Slide 3: SIZE
Size is an important physical attribute of foods used in
Screening solids to separate foreign materials
Grading of fruits and vegetables
Evaluating quality of food materials

## Slide 4
Size of the particulate foods is also critical.
For example ;
Size influences dissolution ability. Particle size of powdered milk must be large enough to prevent agglomeration, but small enough to allow rapid dissolution.
Size of semolina influences its sorption behavior
Size distribution and concentration of particulates present in beverage affect their flavor

## Slide 5
Size grading is used for food operations.
i.e. Cutting, peeling or blending operations
Size grading may also be an indirect means of grading for other quality characteristics. For example smaller-sieve peas are usually less mature and more tender and desirable.

## Slide 6
Particle sizes of particulate foods are expressed in different units:
Coarse particles (i.e. diced apples) are measured in millimeters
Fine particles (i.e. semolina) are measured in terms of screen size
Very fine particles (i.e. Cocoa powder) are measured in micrometers or nanometers

## Slide 7
  For regularly shaped products, 3 characteristic dimensions are defined in size measurement:
  -length (a)
  -width (b)
  -thickness (c)
a
b
c

## Slide 8
These characteristic dimensions are important for uniformity of size.
Because certain devices are adjusted to definite dimensions of material and a restriction is stipulated on the maximum or minimum size.

## Slide 9: SHAPE
Foods of regular geometry are best suited to high speed mechanical processes such as cleaning, peeling of skins, size reduction, sorting, grading, filling into containers, heat processing etc.

## Slide 10
For example;
Potato varieties of smooth shape and with shallow eyes are preferred for mechanical peeling and washing.
Smooth skinned tomatoes are more easily washed than ribbed tomatoes.

## Slide 11
From the view of shape; there are two important processing indices.
These are:
- uniformity of shape
(means that lack of mixed units of irregular size and shapes)
- freedom from surface irregularities

## Slide 12
uniformity of shape
i.e. Roundness of biscuits and hamburgers, sphericity of apples or potatoes, pyriform shape of pear, fusiform shape of cucumbers are desirable shape uniformity characteristics.
These should be considered in filling into containers, conveying, heat transfer, freezing, grading and etc….
12

## Slide 13
freedom from surface irregularities
Surface irregularites cause cleaning and processing problems
The food industry is a labour and energy intensive and raw materials account for a large proportion of the cost of processed foods.

## Slide 14
So,
surface imperfections should be removed either intentially or during processing to contribute significantly to those costs.
Specific varieties must be selected or developed to minimise these defects.
Symmetric products should be used. Why?
14

## Slide 15
Because symmetric products are preferred by consumers.
Asymmetric products are resulted from some additional matters to soil to increase yield.
In food processing symmetric materials are more suitable.

## Slide 16
The shape of a food material is usually expressed in terms of:
  Sphericity and
  Aspect ratio

## Slide 17: Sphericity
*volume of circumscribed sphere means the volume of a sphere that has a diameter equal to the major diameter (length) of the object

## Slide 18: Aspect ratio
The aspect ratio (Ra) is calculated using length (a) and the width (b) of the sample.
=
c
b
a

## Slide 19
Shape has great importance during processes such as;
-in controlling fill-in-weight
-freezing, canning and other heat processes
-in determining the way in which materials behave during pneumatic conveying

## Slide 20: WEIGHT
Weight can be measured by using scales.
Weight can be recorded as:
  Total weight
  Average weight
    Total weight / number of samples
  Weight per unit
    i.e. Weight of a can, weight of a box…

## Slide 21
Most common applications of weight measurements are measurement of weight for canned products.
Weight of a canned product is expressed as :
  Fill-in-weight and
(only contains weight of solid in can, the weight does not include any syrup, brine or other liquid)
  Drained weight
  (weight of solid+liquid)

## Slide 22: VOLUME
Volume is the space occupied by an object.
Volume is an important quality attribute in food industry.
It appeals to the eye and is related to other quality parameters.
For instance, it is inversely proportional to the texture

## Slide 23
Volume of a solid can be determined by using the following methods:
1. Volume can be calculated from the characteristic dimensions in the case of objects with regular shape.
V= a x b x c
a
b
c

## Slide 24
2. Volumes of solids can be determined experimentally by liquid, gas or solid displacement method.
3. Volume can be measured by the image processing method. This method has been developed to measure ellipsoidal products such as eggs, lemons, limes and etc..

## Slide 25: Liquid Displacement Method
If the liquid sample does not absorb liquid very fast,the liquid displacement method can be used to measure its volume.
In this method, sample is put into the liquid containing graduated cylinder. The difference between the initial volume of liquid and volume of liquid with immersed material gives us volume of material.

## Slide 26
Vsolid= Vfinal – Vinitial

## Slide 27
In this method, liquids used should have a low surface tension and slowly absorbed by the particles.
Water, alcohol, toluene are mostly used liquids.
Coating of a sample with a film or paint may be required sometimes to prevent liquid absorption.

## Slide 28: Gas Displacement Method
Volumes of particulate solids and materials with irregular shape can be determined by displacement of gas or air in pycnometer.
Most commonly used gases are helium and nitrogen.

## Slide 29
Figure. Gas Pycnometer

## Slide 30
Pycnometer consists of two airtight chambers of equal volumes, V1 and V2, that are connected to each other.
The material to be measured is placed in the second chamber.
Valve 2 and Valve 3 are closed, initially.
Valve 1 is opened and the gas is supplied to the first chamber until the pressure is increased to a suitable value (e.g. 700-1000 Pa).

## Slide 31
Then the Valve 1 is closed and equilibrium pressure is recorded
(P1V1=nRT1) , (T is constant).
Then Valve 2 is opened and gas within the first chamber is allowed to fill the 2nd chamber. The new pressure (P2) is recorded.

## Slide 32
When valve 2 is opened,total mass of gas (m) is divided into two: one of which fills the first tank (m1) and other fills the space in second tank (m2).
(m=m1 + m2)
Assuming that the system is isothermal.

## Slide 33
P1V1= P2V1 + P2Va2
(Va2 is the volume of empty space in chamber 2)
Va2= V2 - Vs
Vs= volume of solid
Vs= V2- V1 ((P1-P2)/P2)

## Slide 34: Solid Displacement Method
The volume of irregular solids can also be measured by sand, glass bead or seed displacement method.
Rapeseeds are mostly used.
It is not very common.
Sample and rapeseeds are placed together in container.
The container is tapped and the surface is smoothed with a ruler.
Tapping and smoothing are continued until a constant weight is reached.

## Slide 35
Volume of sample can be calculated using following formulas:
Wtotal =Wseeds + Wsample + Wcontainer
Wseeds = Wtotal - Wsample – Wcontainer
Vseeds = Wseeds/ρseeds
Vsample =Vcontainer - Vseeds

## Slide 36
Other volume measurements:
Volume measurement may also be done by:
-Apparent displacement
air spaces between the objects are not considered. Used for units per container, such as number of oranges per box, number of appricots per can…
-Absolute displacement
air spaces between the objects are considered. Similar to the liquid displacement method.